## Slide 1: ROS Calibration and Actions
actionlib and tuning parameters

## Slide 2: Review

## Slide 3: What does ROS do?
At runtime, ROS acts as the nervous system of the robot
ROS is the framework for controlling and coordinating the many components (sensors, motors, tools, logic) that make up the robot
Individual components are called nodes
Nodes can interface with hardware, provide interfaces for users, perform operations, and communicate with other nodes

## Slide 4: Node Communication
ROS nodes typically communicate by sending and receiving messages on various topics
Nodes can also request messages and reply using various services
Nodes can communicate across machines, networks, programming languages, and operating systems

## Slide 5: Node Structure
The ROS Master node handles naming and registration (publishing/subscribing) for all nodes in a ROS system. It must be active in order to run any other node
ROS nodes communicate with each other directly but must first register with the master to find each other
The ROS Master node is instantiated by running roscore or roslaunch in the terminal

## Slide 6: Publisher / Subscriber Model
A node can receive messages by registering a Subscriber and listening to a specific topic
A node can send messages by registering a Publisher and publishing to a specific topic
Messages are defined in .msg files
docs

## Slide 7: Message Example:
Header header
string name
geometry_msgs/PoseWithCovariance pose
geometry_msgs/TwistWithCovariance twist
int32 X=123
string STATE=“Indiana”

## Slide 8: Publisher Example:
1 #!/usr/bin/env python
2
3 import rospy
4 from std_msgs.msg import String
5
6 def talker():
7 pub = rospy.Publisher('chatter', String, queue_size=10)
8 rospy.init_node('talker', anonymous=True)
9 rate = rospy.Rate(10) # 10hz
10 while not rospy.is_shutdown():
11 hello_str = "hello world %s" % rospy.get_time()
12 rospy.loginfo(hello_str)
13 pub.publish(hello_str)
14 rate.sleep()
15
16 if __name__ == '__main__’:
17 try:
18 talker()
19 except rospy.ROSInterruptException:
20 pass

## Slide 9: Request / Reply Model
Nodes can request a message at a specific time (synchronously) by registering a ServiceProxy
Nodes can reply to requests by registering a Service
Services are defined in .srv files
docs

## Slide 10: File System
Software in ROS is organized into packages
Packages can contain ROS nodes, ROS-independent libraries, datasets, configuration files, third-party software, and anything else needed to provide a useful module

## Slide 11: ROS bash commands
rosed
roscd
rosls
rosnode
rostopic
rosservice
rosmsg
rospack
rosdep
rosrun
roslaunch
catkin_create_pkg
catkin_make
Edit a file in a ROS package
Navigate to a package or subdirectory
List files in a package or subdirectory
Work with active nodes
Work with topics
Work with services
Work with messages
Work with packages
Work with
Run a ROS package
Run a ROS launch file
create a catkin package
build a catkin package

## Slide 12: ROS bash commands
rosnode info
        kill
          list
          machine
          ping
          cleanup
print information about node
kill a running node
list active nodes
list nodes running on a given machine or list machines
test connectivity to a node
purge registration information of unreachable nodes

## Slide 13: ROS bash commands
rostopic bw
        delay
          echo
          find
          hz
          info
          list
          pub
          type
display bandwidth used by topic
display delay of a topic
print messages to screen
find topics by type
display publishing rate of topic
print information about active topic
print information about active topics
publish data to topic
print topic type

## Slide 14: Packages
Packages are directories that contain a package.xml file, they tend to look like this:
package_name/
include/package_name
msg/
src/package_name
srv/
scripts/
CMakeLists.txt
package.xml
CHANGELOG.rst
C++ include headers
Folder containing Message types (.msg)
Source files, especially Python source that are exported to other packages
Folder containing Service types (.srv)
Executable scripts
cmake build file for catkin
Description of package
Tracks changes to package

## Slide 15: Catkin
catkin workspaces are used to keep packages organized and build packages
workspace_folder/
  CMakeLists.txt
  package1/
    package.xml
    CMakeLists.txt
    …
    package2/
    package.xml
    CMakeLists.txt
    ….
docs

## Slide 16: TF: Transform Library
Library for keeping track of where your robot is in the world and where each component of your robot is
Simulated and real robots must specify coordinate frames for sensors, motors, COM
tf stores the relationships between coordinate frames as Poses and handles transforms from one frame to another
ROS coordinate frames follow the right-hand rule: x points forward, y points left, z points up

## Slide 17: rviz
ROS Visualization tool

## Slide 18: URDF: Unified Robot Description Format
URDF files specify a robot’s visual model, boundaries, physical properties, and tf frames
Used in visualization, simulation, and interaction of robots
Can include complex meshes created in 3D graphics editors for custom objects

## Slide 19: Today

## Slide 20: Calibration

## Slide 21: Actionlib
The actionlib package provides tools for initiating long-running tasks, getting feedback, cancelling, and
It uses actions to define the goal, feedback, and final output of a task
Ex. Request a robot moves to a point (goal), along the way send its current position (feedback), when it arrives it send a picture from the camera (result)
http://wiki.ros.org/actionlib

## Slide 22: Actionlib: Server

## Slide 23: Actionlib: Client
1 #! /usr/bin/env python
2
3 import roslib
4 roslib.load_manifest('my_pkg_name')
5 import rospy
6 import actionlib
7
8 from chores.msg import DoDishesAction, DoDishesGoal
9
10 if __name__ == '__main__':
11 rospy.init_node('do_dishes_client')
12 client = actionlib.SimpleActionClient('do_dishes', DoDishesAction)
13 client.wait_for_server()
14
15 goal = DoDishesGoal()
16 # Fill in the goal here
17 client.send_goal(goal)
18 client.wait_for_result(rospy.Duration.from_sec(5.0))

## Slide 24: Lab Activity 5
Grab a computer, use your own, or partner up!
If you will be using your own laptop and haven’t installed Ubuntu or ROS please do so. See the installation guide on the course wiki page or the instructors for help
Open Terminal
Go to http://wiki.ros.org/actionlib/Tutorials
Follow 1. Workspace Setup
Then follow exercises 4, 5, and 3 under 2. Beginner Tutorials
WIFI: Westgate-STEM PASSWORD: TheDesignProcess