## Slide 1: Grid Mapping

## Slide 2: Review

## Slide 3: rviz
ROS Visualization tool

## Slide 4: Motion Control
There is a hierarchy of motion controllers in ROS ranging from high-level semantic control to path planning to simple base controllers
The base controller node subscribes to the /cmd_vel topic and translates Twist messages into motor signals that actually turn the wheels.

## Slide 5: Motion Message and Topics
geometry_msgs/Twist:
geometry_msgs/Vector3 linear
  float64 x
  float64 y
  float64 z
geometry_msgs/Vector3 angular
  float64 x
  float64 y
  float64 z
Topics:
/cmd_vel
/cmd_vel_mux
/cmd_vel_mux/input/teleop

## Slide 6: Today

## Slide 7: Occupancy Grid Mapping
A family of computer algorithms for mobile robots which address the problem of generating maps from noisy and uncertain sensor data, assuming that the robot pose is known
The map is represented as an evenly-spaced grid of binary (occupied or unoccupied) random variables. Gmapping computes the probability estimates for individual cells from the robot’s odometry and laser scans.

## Slide 8: Rao-Blackwellized Particle Filter (RBPF)
Used for simultaneous localization and mapping (SLAM)
The RBPF estimates the joint posterior probability of map m and trajectory x1:t of the robot. This estimation is performed given sensor data z1:t and odometry measurements u1:t−1 obtained by the mobile robot.
The factorization allows us to first estimate the trajectory and then compute the map based on the trajectory.
A particle filter of n particles is used to estimate the trajectory, where each particle is a possible x1:t.
gmapping paper

## Slide 9: Gmapping Algorithm
1. {xit} is estimated from the previous {xit-1} and odometry ut-1
2. A scan-matching algorithm (e.g. VASCO) attempts to match the laser scan to the map mit-1 for a set of sampling points around xit, resulting in a probability distribution for each xit
3. New xit are computed from the Gaussian approximation of the scan-matching probability distributions
4. The maps {mit-1} are updated based on the new xit

## Slide 10: Map
2D occupancy grid map of the Freiburg campus
Black cells are occupied
White cells are unoccupied
Grey cells are unseen
Saved as .yaml and .png files

## Slide 11: Octomap
Efficient 3D Occupancy Mapping
Octomap

## Slide 12: Lab Activity 7
Grab a computer, use your own, or partner up!
If you are using your own laptop and haven’t installed Ubuntu or ROS please do so. See the installation guide on the course wiki page or the instructors for help
Open Terminal
Navigate to ROS-Spring2019
git pull
Open the week7 directory and complete the exercises in lab7.txt
WIFI: Westgate-STEM PASSWORD: TheDesignProcess